## Slide 1
MODULE 2 (M2)
SPECIMEN COLLECTION & REFERRAL

## Slide 2: MODULE CONTENTS
  Introduction to the specimen referral system
  TB-specific considerations and requirements for collection, storage, packaging and transport
  Result delivery & electronic
  Monitoring the specimen referral system
* Refers to Xpert MTB/RIF and Xpert MTB/RIF Ultra

## Slide 3: LEARNING OBJECTIVES
At the end of this module, you will be able to:
  Understand the principles of specimen referral systems
  List the TB-specific considerations and recommendations for specimen collection, storage, packaging and transport
  Describe the specimen collection, storage & transport processes
  Tabulate quality indicators for monitoring the specimen referral system

## Slide 4: INTRODUCTION
A well-designed and well-managed specimen referral system underpins a strong diagnostics network
In order to refer specimens from health facilities to laboratories reliably, a comprehensive system is needed that not only includes the needed transport mechanisms and equipment to move specimens, but also includes:
Logistics
Results reporting
Trained personnel
Data management
Monitoring and evaluation
Documentation including a policy framework, standard operating procedures, a comprehensive plan with sufficient financing, and proper governance

## Slide 5: EXAMPLE OF A SPECIMEN REFERRAL SYSTEM*
* www.stoptb.org/wg/gli/assets/documents/GLI_Guide_specimens_web_ready.pdf

## Slide 6: INTRODUCTION
The benefit of specimen referral is to relieve patient of the burden (financial, physical, etc.) to travel to the laboratory  refer the specimen instead of the patient
A well-designed specimen referral system can readily support the referral of many types of specimens for many types of tests
Multiple specimen referral systems can be connected to form an integrated network across a country that meets the needs of various disease programmes
An integrated network can leverage resources of various disease programmes to improve efficiencies and maximize cost-effectiveness of the network and individual referral systems

## Slide 7: INTRODUCTION
The “GLI Guide to TB Specimen Referral Systems and Integrated Networks”* provides design and technical specifications for the handling and transport of specimens for TB testing and builds a case for integrated approaches to specimen referral across sample types and diseases
See Programme Module 3: Plan and establish a sample referral network for TB diagnosis
* www.stoptb.org/wg/gli/assets/documents/GLI_Guide_specimens_web_ready.pdf

## Slide 8: SPUTUM SPECIMEN COLLECTION
The most common diagnostic specimen for TB diagnosis is the expectorated sputum specimen:
Follow the NTP’s guidelines and TB diagnostic algorithm for details on the sample collection for TB diagnosis
See Programme Module 1: Implementing TB diagnostics for WHO recommendations on sample collection for TB diagnosis

## Slide 9: SPUTUM SPECIMEN COLLECTION: CONTAINER SPECIFICATIONS
30-50 ml capacity
Translucent or clear material
Sides and walls that allow easy labelling
Single-use combustible material
Leak-proof with a screw-cap
Wide mouth
To be customized by each country

## Slide 10: SPUTUM SPECIMEN COLLECTION: SAFETY
When providing a sputum specimen, a patient may produce infectious aerosols and therefore biosafety precautions are needed:
  Instruct the patient to cover his or her mouth when coughing
  Never collect sputum in the laboratory
  Collect sputum away from other people in a well ventilated space following the NTP’s guidelines
  Do not stand in front of the patient during specimen collection!

## Slide 11: SPUTUM SPECIMEN COLLECTION: PATIENT EDUCATION AND INSTRUCTIONS
Saliva or nasal secretions are unsatisfactory
Specimens should not contain food or other particles because the test may not work properly
Patients should be instructed to take the following steps to produce the best specimen:
  Wash your mouth with clean water to remove food and other particles
  Inhale deeply 2–3 times and breathe out strongly each time
  Cough deeply from your chest to produce sputum
  Place the open container close to your mouth to collect the specimen; do not get sputum on the outside of the container
  Wash your hands after collecting the sample

## Slide 12: SPUTUM SPECIMEN COLLECTION: GOOD QUALITY
Obtaining an adequate quantity of good quality sputum is critical to ensuring accurate test results
For best results, obtain >1ml of purulent/mucoid sputum
Purulent
Mucoid
Bloodstained
Photo credit A. van Deun

## Slide 13: SPUTUM SPECIMEN COLLECTION: POOR QUALITY
Poor quality specimens give poor quality results
Salivary (thin, watery, or comprised mainly of bubbles)
Photo credit A. van Deun

## Slide 14: SPUTUM SPECIMEN COLLECTION: LABELLING
Label with the patient’s name, identification number and the date of collection
Label the outer sides of the container with permanent ink
Never label the lid
Complete the Laboratory Request Form. See Technology Module 4: Recording & reporting results
Once specimens are collected and labelled, they can be packaged and referred to laboratory for testing

## Slide 15: SPUTUM SPECIMEN COLLECTION: REQUEST FORMS
To be customized by each country
Add your request form here, and show participants how to correctly complete the form. Does it include:
Name of the treatment unit
Date of the request
Patient's information (that is, name, sex, age, address and the register number of the patient or suspected case)
Number of specimens and types of specimens sent for testing
Date the specimens were collected
Reason for examination (for example, diagnosis or follow-up)
Signature of the person requesting the examination

## Slide 16: EXERCISE 1: PROPERLY FILLING NTP REQUISITION FORM
Purpose
The objective of this exercise is to complete a Laboratory Request Form with the information provided
Total time
25 minutes
Instructions
All participants divide into groups (up to 5 groups are permissible)
Assign each group a number (see above)
Each group to complete the Laboratory Request Form with the information provided
Groups to present their completed Laboratory Request Form for discussion

## Slide 17: SPUTUM SPECIMEN PACKAGING: TRIPLE-PACKAGING TO ENSURE BIOSAFETY
Primary packaging
Wrap the leak-proof container in cotton wool or paper towels in a sufficient quantity to absorb the entire contents in case of leaks
Secondary packaging
Place the wrapped container inside a secondary container, such as a self-sealing plastic bag or another container
Place secondary container in a rack to prevent leakage

## Slide 18: UM SPECIMEN PACKAGING: TRIPLE-PACKAGING TO ENSURE BIOSAFETY
Tertiary packaging
Place the secondary container and its contents in an approved safety cooler box or another appropriate container in an upright position
Place a biohazard sign – with markings and labelling appropriate for the specimen category – on the tertiary container

## Slide 19: SPECIMEN TRANSPORT GUIDELINES
  SOPs for occurrence management (i.e. for documenting spills, delays or lost samples), including who to contact in the event of an occurrence should be available to transporters/ couriers
  Transporters or couriers should have access to a spill kit
Transporters or couriers should be trained on what to do in the case of an accident or spill

## Slide 20: SPECIMEN TRANSPORT GUIDELINES
Total number of specimens in a box must correspond to the number of accompanying Laboratory Request Forms
Identification number on each sputum container must correspond to the number on a request form
Accompanying forms must contain the required information for each patient
Documentation should accompany specimens to show Chain of Custody (signed by referring health facility, transporter and laboratory) for tracking
SOPs should be available for transportation of specimens
To be customized by each country

## Slide 21: HANDOFF TO COURIER OR TRANSPORTER
Sign the courier logbook/shipping forms to show chain of custody
Referring facilities should maintain a Sample transportation logbook to keep track of samples that has been sent /referred for testing. This will allow them to keep track of how many samples they should receive results for and monitor if results do not come back
Hand over properly-packaged specimens to the courier/ transporter – it is not usually their responsibility to package the specimens, only to transport

## Slide 22: EXAMPLE SAMPLE TRANSPORTATION LOGBOOK*
* www.stoptb.org/wg/gli/assets/documents/GLI_Guide_specimens_web_ready.pdf

## Slide 23: REQUIREMENTS, STORAGE & TRANSPORT OF SPECIMENS: SMEAR MICROSCOPY
Number of samples: 2
Minimum volume: 1 ml for direct microscopy; 3–5 ml if samples are to be concentrated
Storage / shipping conditions: For sputum samples for AFB-smear microscopy, viability is not an issue and storage and transport at ambient temperature (20–30°C) for a total of 1 to 2 days or storage and transport at 2–8°C for a total of up to a week will not significantly affect the positivity

## Slide 24
Number of samples: A single sputum specimen is recommended for Xpert MTB/RIF (Ultra) testing:
  An additional sputum specimen may be needed in case of an error or invalid Xpert MTB/RIF (Ultra) result
  An additional sputum is required for re-testing of Xpert MTB/RIF Ultra trace results*
  Additional sputum specimens may be needed for microscopy, culture and DST, depending on the NTP’s guidelines [Xpert MTB/RIF (Ultra) are not recommended for monitoring patient treatment]
* http://www.stoptb.org/wg/gli/assets/documents/GLI_ultra.pdf
REQUIREMENTS, STORAGE & TRANSPORT OF SPECIMENS: XPERT MTB/RIF (ULTRA)

## Slide 25
Minimum volume: 1 ml, 2–4 ml samples are preferred
Storage / shipping conditions: For sputum samples being transported for Xpert MTB/RIF (Ultra) testing, viability is not an issue, but stability of nucleic acids is a consideration:
Whenever possible, samples should be stored at 2-8 °C prior Xpert MTB/RIF (Ultra) testing and during transportation. If necessary, specimens may be stored at ambient temperature (max 35°C) for up to 3 days, then refrigerated at 2-8°C)
REQUIREMENTS, STORAGE & TRANSPORT OF SPECIMENS: XPERT MTB/RIF (ULTRA)

## Slide 26
REQUIREMENTS, STORAGE & TRANSPORT OF SPECIMENS: NUCLEIC AMPLIFICATION TESTING
Number of samples: A single sputum sample is required
Minimum volume: 1 ml, 2–4 ml samples are preferred
Storage / shipping conditions: For sputum samples being transported for Line Probe Assay (LPA), viability is not an issue, but stability of nucleic acids is a consideration- see Xpert MTB/RIF (Ultra) recommendations
Note: some samples may require additional culture and phenotypic DST if the LPA result detects resistance. These samples require more stringent handling (see culture recommendations)

## Slide 27: REQUIREMENTS, STORAGE & TRANSPORT OF SPECIMENS: CULTURE
Minimum volume: 3–5 ml
The two most important considerations for transporting sputum specimens for culture tests, in addition to biosafety, are:
Preserving the viability of the mycobacteria
Inhibiting the growth of contaminating flora
Viability of tubercle bacilli can be maintained for up to 7 days by keeping the specimens at 2–8°C
Contaminating flora may grow under these conditions and result in increased contamination rates for the culture tests

## Slide 28: REQUIREMENTS, STORAGE & TRANSPORT OF SPECIMENS: CULTURE
For solid culture, if the delay (storage and transport) exceeds 3 days and storage at 2–8°C is not possible, cetyl pyridinium chloride (CPC) may be added to the sputum specimen to inhibit growth of the contaminating flora
Sputum specimens containing CPC must be stored at ambient temperature (20–30°C) and be delivered to the testing laboratory within 7 days
CPC recrystallizes at cool temperatures which removes its ability to protect the specimen from contamination
CPC can’t be used in liquid culture systems such as BACTEC MGIT*
* https://www.ncbi.nlm.nih.gov/pmc/articles/PMC5543576/

## Slide 29: REQUIREMENTS, STORAGE & TRANSPORT OF SPECIMENS: CULTURE
Products that can be used instead of CPC to preserve specimens for culture are commercially available (e.g., OMNIgene•SPUTUM from DNA Genotek Ottawa, Canada)
A recent WHO Technical Expert Group* meeting concluded that there is limited evidence that use of commercial transport products improves test performance compared to untreated specimens transported under ambient conditions for culture
* http://www.who.int/tb/areas-of-work/laboratory/policy_statements/

## Slide 30: REQUIREMENTS, STORAGE & TRANSPORT OF SPECIMENS: OTHER THAN SPUTUM
Little information is available on the stability of tubercle bacilli in specimens other than sputum
Bronchoalveolar lavage fluid, neutralized gastric aspirates, tissue specimens and cerebrospinal fluid (CSF) should be transported to the testing laboratory immediately, preferably on the same day as collection
Great care (i.e., storage and transport at the proper temperature, immediate transport to the laboratory, and immediate testing at the laboratory) must be taken to ensure the quality and utility of invasively obtained specimens such as tissue biopsies and CSF. This is due to the difficulty of obtaining repeat specimens for retesting and the urgent nature of testing on such samples

## Slide 31: SPECIMEN RECEPTION AT LABORATORY: DROP OFF POINT
Specimens should be received by an individual designated for specimen reception at the laboratory
  Laboratory signs Chain of Custody/shipment form to record receipt of specimens
  Referral lab maintains a logbook where specimen received are recorded
  Laboratory performs quality check of specimens against rejection criteria
Specimen reception area may also be collection point for results

## Slide 32: EXAMPLE OF A TB SPECIMEN REFERRAL REGISTER*
* www.stoptb.org/wg/gli/assets/documents/GLI_Guide_specimens_web_ready.pdf

## Slide 33: SAMPLE REJECTION CRITERIA: XPERT MTB/RIF (ULTRA)
  No or incomplete Laboratory Request Form
  Specimen leaked in transit
Important to understand rejection criteria for Xpert MTB/RIF (Ultra):
  Less than 1ml specimen
  Particles in specimen
  Specimen not suitable, i.e. urine, stool, blood
  ALSO- general sample rejection criteria (see previous)
To be customized by each country

## Slide 34: RESULT DELIVERY & ELECTRONIC REPORTING
An electronic reporting system is recommended for reporting results to clinicians*
If a paper-based system in used:
  Results should follow the same transportation route/ mechanism as specimens (in reverse), if paper result is returned
  Other supplies may also be collected at the same time and brought to the health facility
  Results can be collected when specimens are dropped off at the laboratory
  Laboratory signs Chain of Custody/shipment form to record release of results
* http://www.stoptb.org/wg/gli/assets/documents/gli_connectivity_guide.pdf

## Slide 35: RESULT DELIVERY & ELECTRONIC REPORTING
Connectivity solutions typically comprise:
  A connectable diagnostic device that produces electronic data,
  A software platform that receives and interprets data,
  A means to transmit data from the device to the software platform and to a server
Systems have been developed by Cepheid, USA (C360), SystemOne (GxAlert™/Aspect™), Savics (DataToCare™) and FIND (Connected Diagnostics Platform)

## Slide 36: RESULT DELIVERY & ELECTRONIC REPORTING
Test results can be sent to the NTPs electronically as real-time data to assist with surveillance
Electronic reporting can enhance the capacity of NTPs to generate performance indicators and to provide the data needed for several of the top 10 indicators of the End TB Strategy
Another key feature of electronic systems are to send results automatically to clinicians and automatically into LIMSs and electronic registers

## Slide 37: SPECIMEN REFERRAL TO OTHER LABOTATORIES
If specimens will be referred to a testing laboratory outside of the collection facility, they need to be packaged properly to ensure safe transit and quality control, and documented to track chain of custody:
  Fill out requisition and shipping forms properly
  Triple packaging for biosafety reasons
  Hand-off to couriers or person who will transport specimen to laboratory, if necessary

## Slide 38: INDICATORS TO MONITOR SPECIMEN REFERRAL
Monitoring and evaluation for specimen referral systems should examine the performance of the whole system (high level as well as its operations at a more detailed level)
Quality indicator monitoring requires:
Standardizing registers and forms
Quality control practices during specimen collection, packaging and transport
Targets should be set for all indicators, and any unexplained change in quality indicators, should be documented and investigated

## Slide 39
Indicators that should be monitored monthly by the referring facility
Number of specimens referred for testing
Proportion of referred specimens for which a result was returned
Proportion of referred specimens for which a result was received within the target turnaround time
Proportion of specimens which were picked up by the transport service within the target turnaround time
Indicators that should be monitored monthly by the receiving (referral) laboratory
Number of referred specimens tested at the referral laboratory
Proportion of shipments that arrive at the referral laboratory within the specified transport time
Proportion of test results that were picked up by the transport service or transmitted electronically within the specified turnaround time after generation of the test result
Proportion of specimens that were rejected because of factors related to inadequate or improper transport, packaging or documentation (disaggregated by referring site)
QUALITY INDICATOR MONITORING
Adapt according to NTP guidelines in your country

## Slide 40
Indicators that should be monitored monthly by the courier as part of their service agreement
Number of shipments and number of specimens transported
Proportion of shipments that are delivered within the specified transport time
Proportion of shipments that were lost or damaged (disaggregated by route or district)
Indicators that should be monitored annually at the regional or national level by the TWG or MoH
Number of specimen collection sites participating in the specimen referral system
Unit costs such as cost per specimen or result transported per facility or per month
Annual review of consolidated indicators for each region and for the country
QUALITY INDICATOR MONITORING
Adapt according to NTP guidelines in your country

## Slide 41: DISCUSSION QUESTIONS
Describe the process of sputum collection
Describe the process for triple packaging a specimen
What are the specimen requirements for Xpert MTB/RIF (Ultra) testing?
What are the storage & transport requirements for Xpert MTB/RIF (Ultra) samples?
List two quality indicators that should be collected by the referring facility

## Slide 42: KEY MESSAGES
A well-designed and well-managed specimen referral system underpins a strong diagnostics network
Proper collection, storage and transport procedures are need to be followed to ensure specimen quality and biosafety
All specimen referrals must be tracked
Results should follow the same transport pathway/mechanism as specimens, but in reverse
Electronic reporting of results should be prioritised
Targets should be set for all indicators collected to monitor sample referral. Any unexplained change in quality indicators, should be documented and investigated

## Slide 43
THANK YOU
© John Rae