## Slide 1
MODULE 3 (M3)
PROCUREMENT AND INVENTORY MANAGEMENT

## Slide 2: CONTENTS OF THIS MODULE
Product selection
Procurement for Xpert MTB/RIF (Ultra)*
Distribution
Stock control including storage and shelf life of supplies
* Refers to Xpert MTB/RIF and Xpert MTB/RIF Ultra

## Slide 3: LEARNING OBJECTIVES
At the end of this module, you will be able to:
List all supplies required for performing the Xpert MTB/RIF (Ultra) tests
Forecast supplies needed based on the number of tests performed during a specific period
Describe the procurement processes
Explain the use and importance of the stock log book in maintaining an adequate inventory
Explain storage and shelf life requirements of Xpert MTB/RIF (Ultra) kits

## Slide 4: GOOD SUPPLY MANAGEMENT ENSURES…
…properly maintained and adequate supplies for uninterrupted diagnostic services with minimal waste

## Slide 5: GOOD SUPPLY MANAGEMENT ENSURES…
Effective supply chain management is a complex process that includes:
  Product selection
  Product specification
  Forecasting of needs (based on past and projected consumption)
  Procurement and the ordering
  Customs clearance, if applicable
  Distribution
  Stock management including storage and use
  Monitoring the supply chain

## Slide 6: SUPPLY CHAIN MANAGEMENT PROCESS
Selection
Procurement
Distribution
Use
Forecasting
Monitoring & evaluation
Stock management
Storage
Product specification
Ordering

## Slide 7: INTRODUCTION
An inadequately managed supply chain may result in either under- or over-stocking supplies:
If access to supplies are interrupted, a laboratory may have to suspend services and/or divert patients to other testing sites. This may result in delayed diagnosis of patients, and confusion and lack of confidence in the laboratory by clinicians
Over-stocking also has negative consequences, including waste of resources when stock reaches its expiry date before being consumed

## Slide 8: SUPPLY CHAIN MANAGEMENT
Managing supplies involves careful planning and coordination, and should follow the well-recognized cycles of selection, procurement, distribution, and use
General guidance can be obtained from various sources, including “USAID/Deliver: Guidelines for Managing the Laboratory Supply Chain (2008)” and WHO “Guidance for countries on the specifications for managing TB laboratory equipments and supplies (2011)”

## Slide 9: SUPPLY MANAGEMENT SYSTEM
Describe the supply management system(s) in your country

## Slide 10: PRODUCT SELECTION
Use standard testing protocols to develop a commodity list (reagents, consumable & durables). Consider the following:
Cost and available ﬁnancing
Storage requirements, such as cold chain, and capacity to maintain the commodities
Skill level of personnel (or training requirements)
Ease of use of the commodity
Packaging of the commodities to facilitate distribution
Shelf life
Compatibility with existing instrumentation (durables)

## Slide 11: INFORMATION NEEDED FOR FORECASTING OF GENEXPERT SUPPLIES
Type of GeneXpert cartridges to be ordered [e.g. Xpert MTB/RIF (Ultra)]
Additional items not supplied with kit
Catalogue numbers
Delivery Address
Contact details of receiving party
Available digital systems (e.g. GXAlert) can be used to support forecasting
Describe the system for procurement of GeneXpert supplies in your country

## Slide 12: CONTENT OF GENEXPERT KIT
Assay Cartridges
Sample Reagent (8mL – one per test)
Disposable transfer pipettes (one per test)
CD containing the Assay Definition File

## Slide 13: GENEXPERT: ITEMS REQUIRED BUT NOT PROVIDED
Biohazard supplies:
    Bio-hazard bags for waste disposal
  Suitable disinfectant (phenolic, bleach solution,70% alcohol, etc.) and containers for preparation and use
  Discard containers (for pipettes, sputum containers and used cartridges)
  Contents of spill kit

## Slide 14: GENEXPERT: ITEMS REQUIRED BUT NOT PROVIDED
Personal protective equipment:
Laboratory coats
Gloves
Respirators (optional)
Laboratory supplies:
Paper towels (for cleaning bench tops and external surfaces of instrument)
Soft tissue paper (for cleaning cartridge bays and plunger)
Sample storage containers e.g. box or tray

## Slide 15: GENEXPERT: ITEMS REQUIRED BUT NOT PROVIDED
Stationery supplies:
Laboratory registers and request/report forms
Permanents markers
Pens (red; blue or black)
Write-on stickers (optional)
Barcodes (optional)
Printing paper (optional)
Printer ink (optional)

## Slide 16: ORDERING & DISTRIBUTION
In well-functioning programmes, forecasting, procurement, and distribution are under regulation by a national system
Central data systems monitor both distribution and consumption rates for all laboratories
Materials and supplies are stored in well-organized national warehouses with proper climate control conditions
Distribution is then provided on a schedule which correlates to usage rates
Shipments to laboratories are organized on a central calendar to ensure timely delivery
Often regional hubs are established to facilitate local transit or pickups

## Slide 17: DISTRIBUTION NETWORKS*
* www.stoptb.org/wg/gli/assets/documents/GLI_practical_guide.pdf

## Slide 18: STOCK MANAGEMENT
Have a designated person for supply management to perform the following:
  Do a monthly “stock count”
  Maintain inventory records
  Determine how much to order to avoid stock-outs and expiring of cartridges
  Place orders in accordance with local ordering practices
  Inspect and verify supplies received
  Ensure proper storage of stock

## Slide 19: UPON RECEIPT
Inspect & verify the delivery of the order:
Verify contents of order received matches quantity requested
Check integrity of received supplies
Note the date each item was received
Create or update records
Perform new lot testing (see Module M6: Quality Assurance of the Xpert MTB/RIF (Ultra))

## Slide 20: PROPER STORAGE OF INVENTORY
GeneXpert kits must be kept at 2-28C
Store away from direct sunlight
Store kits the correct way up
Organize existing and new shipments by expiry date so that supplies with the soonest expiry date must be used first- “FIRST EXPIRY – FIRST OUT” (FEFO)

## Slide 21: XPERT MTB/RIF ULTRA SUPPLY CHAIN CONSIDERATIONS
Xpert MTB/RIF Ultra cartridges had a limited shelf life at product launch. The targeted shelf life for Xpert Ultra is 24 months (same as Xpert MTB/RIF). The current shelf life should be requested from the manufacturer or procurement agent at the time of forecasting and order placement.
The Xpert MTB/RIF and Xpert MTB/RIF Ultra cartridges are almost visually identical, except for the labelling and the reaction ‘fin’. Extreme care should be taken to segregate stocks and ensure the correct cartridges are used

## Slide 22: XPERT MTB/RIF ULTRA SUPPLY CHAIN CONSIDERATIONS
In contrast to the Xpert MTB/RIF 10-test kit, the Xpert MTB/RIF Ultra 10-test kit does not include a cartridge pouch to enclose each cartridge
Both 50-test kits have five pouches, each enclosing 10 cartridges
Sites that will use Xpert MTB/RIF Ultra cartridges need to run GeneXpert software version 4.7b or later. Procurement plans may need to take into consideration the time required to update sites’ software.

## Slide 23: STOCK LOG: REQUIRED DATA
Date and amount ordered
Date of receipt of item
Amount received
Lot-number
Expiry date
Amount of used items
Balance of items still in stock

## Slide 24: STOCK CARD: EXAMPLE
Physical count |  | Requested |  | Received |  | Stock in hand | Signature
Units (No) | Date | Units (No) | Date | Units (No) | Date |  | 
Item name: ________________ Unit: ______________________
Notes: Fill this in to be used in exercise

## Slide 25: MONITORING THE SUPPLY CHAIN
Monitoring stock outs is an essential quality indicator for managing the supply chain
Other quality indicators that can be monitored include:
  Order fulfilment lead time
Fulfilment of orders on time
Damage-free delivery
Complete delivery as required
Delivery meets laboratory requirements
Perfect order fulfilment

## Slide 26: STOCK CALCULATION EXAMPLE
The aim of this activity is to correctly forecast reagent testing requirements:
Review the examples on the following slides as a group
Then work in pairs to complete Exercise 1
  For feedback, 2 people picked at random will talk through 1 answer each
  Exercise will take 30 minutes

## Slide 27: DATA REQUIRED FOR FORECASTING
Average number of items required for the order time period = (A)
Quantity of items needed per test = (B)
Quantity of an item required for one month = (C)
Buffer/reserve stock = (D)

## Slide 28: DATA REQUIRED FOR FORECASTING
Stock currently available (physical count) = (E)
Amount of stock currently needed by the laboratory to be able to continue testing for 1 quarter, plus buffer considering what the lab already has currently available = (F)
The unit in which stock can be ordered = (G)
Amount to be requested considering the pack size = (H)

## Slide 29: CALCULATE A
A is equal to the average number of items required for the order time period.
  Time period of order = Quarterly
  Number of tests site performs per day = 10
  Number of days the lab works in a month = 20
Calculate the average quarterly consumption
= 10 tests x 20 days in a month x 3 months
= 600 tests per quarter

## Slide 30: CALCULATE QUARTERLY REQUIREMENT FOR LABORATORY REQUEST
Quarterly Supply requirements for Xpert MTB/RIF Ultra testing |  |  |  |  |  |  | 
Laboratory Regional reference laboratory |  |  |  |  |  |  | 
Region Western Region |  |  |  | Supply Quarter 3 |  |  | 
District Urban |  |  |  | Year 2016 |  |  | 
Total tests performed in previous quarter, including failed tests (A) 600 |  |  |  |  |  |  | 
Items | Quantity needed per test (B) | Stock for one month (C) =(A/3)*B | Stock for quarter with 1 month buffer (D)= C*4 | Stock on hand (E) | Calculated request (F) = D-E | Order unit (G) | Actual order (H) = F/G and round up
Sputum container |  |  |  |  |  |  | 
Xpert MTB/RIF Ultra |  |  |  |  |  |  | 
Concentrated bleach (L) |  |  |  |  |  |  | 
Notes: EDIT

## Slide 31: CALCULATE (B)
Calculate the quantity of items required to perform one Xpert Ultra testing

## Slide 32: CALCULATE QUARTERLY REQUIREMENT FOR LABORATORY REQUEST
Quarterly Supply requirements for Xpert MTB/RIF Ultra testing |  |  |  |  |  |  | 
Laboratory Regional reference laboratory |  |  |  |  |  |  | 
Region Western Region |  |  |  | Supply Quarter 3 |  |  | 
District Urban |  |  |  | Year 2016 |  |  | 
Total tests performed in previous quarter, including failed tests (A) 600 |  |  |  |  |  |  | 
Items | Quantity needed per test (B) | Stock for one month (C) =(A/3)*B | Stock for quarter with 1 month buffer (D)= C*4 | Stock on hand (E) | Calculated request (F) = D-E | Order unit (G) | Actual order (H) = F/G and round up
Sputum container | 1 |  |  |  |  |  | 
Xpert MTB/RIF Ultra | 1 |  |  |  |  |  | 
Concentrated bleach (L) | 0.0015 |  |  |  |  |  | 
Notes: EDIT

## Slide 33: CALCULATE C
The value (C) equals the quantity of an item required for one month
Calculate (C) by dividing the number of tests performed during a quarter (A) by 3 months. Then multiply that number by the amount of the item needed for one examination (B)
Therefore: A/3 x B = C

## Slide 34: CALCULATE QUARTERLY REQUIREMENT FOR LABORATORY REQUEST
Quarterly Supply requirements for Xpert MTB/RIF Ultra testing |  |  |  |  |  |  | 
Laboratory Regional reference laboratory |  |  |  |  |  |  | 
Region Western Region |  |  |  | Supply Quarter 3 |  |  | 
District Urban |  |  |  | Year 2016 |  |  | 
Total tests performed in previous quarter, including failed tests (A) 600 |  |  |  |  |  |  | 
Items | Quantity needed per test (B) | Stock for one month (C) =(A/3)*B | Stock for quarter with 1 month buffer (D)= C*4 | Stock on hand (E) | Calculated request (F) = D-E | Order unit (G) | Actual order (H) = F/G and round up
Sputum container | 1 | 200 |  |  |  |  | 
Xpert MTB/RIF Ultra | 1 | 200 |  |  |  |  | 
Concentrated bleach (L) | 0.0015 | 0.3 L |  |  |  |  | 
Notes: EDIT

## Slide 35: CALCULATE D
The value (D) equals the quantity of an item required for one Quarter + additional 1 month buffer stock
Calculate (D) by determining (C) (i.e. multiplying the number of tests performed during a month (A) by the amount of the item needed for one examination (B)
Therefore: A/3 x B = C
D = C x 4

## Slide 36: CALCULATE QUARTERLY REQUIREMENT FOR LABORATORY REQUEST
Quarterly Supply requirements for Xpert MTB/RIF Ultra testing |  |  |  |  |  |  | 
Laboratory Regional reference laboratory |  |  |  |  |  |  | 
Region Western Region |  |  |  | Supply Quarter 3 |  |  | 
District Urban |  |  |  | Year 2016 |  |  | 
Total tests performed in previous quarter, including failed tests (A) 600 |  |  |  |  |  |  | 
Items | Quantity needed per test (B) | Stock for one month (C) =(A/3)*B | Stock for quarter with 1 month buffer (D)= C*4 | Stock on hand (E) | Calculated request (F) = D-E | Order unit (G) | Actual order (H) = F/G and round up
Sputum container | 1 | 200 | 800 |  |  |  | 
Xpert MTB/RIF Ultra | 1 | 200 | 800 |  |  |  | 
Concentrated bleach (L) | 0.0015 | 0.3 L | 1.2 L |  |  |  | 
Notes: EDIT

## Slide 37: CALCULATE E
E is the amount of stock currently available in the laboratory or store
Review the stock card, or complete a stock count

## Slide 38: CALCULATE QUARTERLY REQUIREMENT FOR LABORATORY REQUEST
Quarterly Supply requirements for Xpert MTB/RIF Ultra testing |  |  |  |  |  |  | 
Laboratory Regional reference laboratory |  |  |  |  |  |  | 
Region Western Region |  |  |  | Supply Quarter 3 |  |  | 
District Urban |  |  |  | Year 2016 |  |  | 
Total tests performed in previous quarter, including failed tests (A) 600 |  |  |  |  |  |  | 
Items | Quantity needed per test (B) | Stock for one month (C) =(A/3)*B | Stock for quarter with 1 month buffer (D)= C*4 | Stock on hand (E) | Calculated request (F) = D-E | Order unit (G) | Actual order (H) = F/G and round up
Sputum container | 1 | 200 | 800 | 100 |  |  | 
Xpert MTB/RIF Ultra | 1 | 200 | 800 | 300 |  |  | 
Concentrated bleach (L) | 0.0015 | 0.3 L | 1.2 L | 0.5 L |  |  | 
Notes: EDIT

## Slide 39: CALCULATE F
F is the amount of stock currently needed by the laboratory to be able to continue testing for 1 quarter, plus buffer considering what the lab already has currently available
Therefore: F= D-E

## Slide 40: CALCULATE QUARTERLY REQUIREMENT FOR LABORATORY REQUEST
Quarterly Supply requirements for Xpert MTB/RIF Ultra testing |  |  |  |  |  |  | 
Laboratory Regional reference laboratory |  |  |  |  |  |  | 
Region Western Region |  |  |  | Supply Quarter 3 |  |  | 
District Urban |  |  |  | Year 2016 |  |  | 
Total tests performed in previous quarter, including failed tests (A) 600 |  |  |  |  |  |  | 
Items | Quantity needed per test (B) | Stock for one month (C) =(A/3)*B | Stock for quarter with 1 month buffer (D)= C*4 | Stock on hand (E) | Calculated request (F) = D-E | Order unit (G) | Actual order (H) = F/G and round up
Sputum container | 1 | 200 | 800 | 100 | 700 |  | 
XpertMTB/RIF Ultra | 1 | 200 | 800 | 300 | 500 |  | 
Concentrated bleach (L) | 0.0015 | 0.3 L | 1.2 L | 0.5 L | 0.7 |  | 
Notes: EDIT

## Slide 41: CALCULATE G
G is the unit in which stock can be ordered
  i.e. Xpert Ultra kits come as pack sizes of 50

## Slide 42: CALCULATE QUARTERLY REQUIREMENT FOR LABORATORY REQUEST
Quarterly Supply requirements for Xpert MTB/RIF Ultra testing |  |  |  |  |  |  | 
Laboratory Regional reference laboratory |  |  |  |  |  |  | 
Region Western Region |  |  |  | Supply Quarter 3 |  |  | 
District Urban |  |  |  | Year 2016 |  |  | 
Total tests performed in previous quarter, including failed tests (A) 600 |  |  |  |  |  |  | 
Items | Quantity needed per test (B) | Stock for one month (C) =(A/3)*B | Stock for quarter with 1 month buffer (D)= C*4 | Stock on hand (E) | Calculated request (F) = D-E | Order unit (G) | Actual order (H) = F/G and round up
Sputum container | 1 | 200 | 800 | 100 | 700 | 1000 per pack | 
Xpert MTB/RIF Ultra | 1 | 200 | 800 | 300 | 500 | 50 per kit | 
Concentrated bleach (L) | 0.0015 | 0.3 L | 1.2 L | 0.5 L | 0.7 | 1L per bottle | 
Notes: EDIT

## Slide 43: CALCULATE H
H is the amount to be requested considering the pack size
Therefore: H = F/G and rounded up to the next pack size

## Slide 44: CALCULATE QUARTERLY REQUIREMENT FOR LABORATORY REQUEST
Quarterly Supply requirements for Xpert MTB/RIF Ultra testing |  |  |  |  |  |  | 
Laboratory Regional reference laboratory |  |  |  |  |  |  | 
Region Western Region |  |  |  | Supply Quarter 3 |  |  | 
District Urban |  |  |  | Year 2016 |  |  | 
Total tests performed in previous quarter, including failed tests (A) 600 |  |  |  |  |  |  | 
Items | Quantity needed per test (B) | Stock for one month (C) =(A/3)*B | Stock for quarter with 1 month buffer (D)= C*4 | Stock on hand (E) | Calculated request (F) = D-E | Order unit (G) | Actual order (H) = F/G and round up
Sputum container | 1 | 200 | 800 | 100 | 700 | 1000 per pack | 1 pack
Xpert MTB/RIF Ultra | 1 | 200 | 800 | 300 | 500 | 50 per kit | 10 kits
Concentrated bleach (L) | 0.0015 | 0.3 L | 1.2 L | 0.5 L | 0.7 | 1L per bottle | 1 bottle
Notes: EDIT

## Slide 45: EXERCISE 1: FORECASTING
Calculation #1
Time period of order = Quarterly
Number of Xpert MTB/RIF tests site performs per day = 10
The lab works 21 days a month
The lab uses 0.0015L bleach /test
Calculation #2
Time period of order = Quarterly
Number of Xpert MTB/RIF Ultra tests site performs per day = 5
The lab works 25 days a month
The lab uses 0.0015L bleach /test
Calculation #3
Time period of order = Quarterly
Number of Xpert MTB/RIF Ultra tests site performs per day = 12
The lab works 21 days a month
The lab uses 0.0015L bleach /test

## Slide 46: ASSUMPTION FOR CALCULATION #1
Quarterly Supply requirements for Xpert MTB/RIF testing |  |  |  |  |  |  | 
Laboratory Regional reference laboratory |  |  |  |  |  |  | 
Region Western Region |  |  |  | Supply Quarter 3 |  |  | 
District Urban |  |  |  | Year 2016 |  |  | 
Total tests performed in previous quarter, including failed tests (A) |  |  |  |  |  |  | 
Items | Quantity needed per test (B) | Stock for one month (C) =(A/3)*B | Stock for quarter with 1 month buffer (D)= C*4 | Stock on hand (E) | Calculated request (F) = D-E | Order unit (G) | Actual order (H) = F/G and round up
Sputum container |  |  |  | 30 |  | 100 pack | 
Xpert MTB/RIF |  |  |  | 100 |  | 50 kit | 
Concentrated bleach (L) |  |  |  | 0.25L |  | 1L bottle | 
Notes: EDIT

## Slide 47: ANSWER FOR CALCULATION #1
Quarterly Supply requirements for Xpert MTB/RIF testing |  |  |  |  |  |  | 
Laboratory Regional reference laboratory |  |  |  |  |  |  | 
Region Western Region |  |  |  | Supply Quarter 3 |  |  | 
District Urban |  |  |  | Year 2016 |  |  | 
Total tests performed in previous quarter, including failed tests (A) 630 |  |  |  |  |  |  | 
Items | Quantity needed per test (B) | Stock for one month (C) =(A/3)*B | Stock for quarter with 1 month buffer (D)= C*4 | Stock on hand (E) | Calculated request (F) = D-E | Order unit (G) | Actual order (H) = F/G and round up
Sputum container | 1 | 210 | 840 | 30 | 810 | 100 pack | 9 packs
Xpert MTB/RIF | 1 | 210 | 840 | 100 | 740 | 50 kit | 15 kits
Concentrated bleach (L) | 0.0015 | 0.315 | 1.26 | 0.25L | 1.01 | 1L bottle | 2 bottles
Notes: EDIT

## Slide 48: ASSUMPTIONS FOR CALCULATION #2
Quarterly Supply requirements for Xpert MTB/RIF Ultra testing |  |  |  |  |  |  | 
Laboratory Regional reference laboratory |  |  |  |  |  |  | 
Region Western Region |  |  |  | Supply Quarter 3 |  |  | 
District Urban |  |  |  | Year 2016 |  |  | 
Total tests performed in previous quarter, including failed tests (A) |  |  |  |  |  |  | 
Items | Quantity needed per test (B) | Stock for one month (C) =(A/3)*B | Stock for quarter with 1 month buffer (D)= C*4 | Stock on hand (E) | Calculated request (F) = D-E | Order unit (G) | Actual order (H) = F/G and round up
Sputum container |  |  |  | 75 |  |  | 100 pack
Xpert MTB/RIF Ultra |  |  |  | 20 |  |  | 10 kit
Bleach (L) |  |  |  | 1L |  |  | 4L bottle
Notes: EDIT

## Slide 49: ANSWER FOR CALCULATION #2
Quarterly Supply requirements for Xpert MTB/RIF Ultra testing |  |  |  |  |  |  | 
Laboratory Regional reference laboratory |  |  |  |  |  |  | 
Region Western Region |  |  |  | Supply Quarter 3 |  |  | 
District Urban |  |  |  | Year 2016 |  |  | 
Total tests performed in previous quarter, including failed tests (A) 375 |  |  |  |  |  |  | 
Items | Quantity needed per test (B) | Stock for one month (C) =(A/3)*B | Stock for quarter with 1 month buffer (D)= C*4 | Stock on hand (E) | Calculated request (F) = D-E | Order unit (G) | Actual order (H) = F/G and round up
Sputum container | 1 | 125 | 500 | 75 | 425 | 100 pack | 5 packs
Xpert MTB/RIF Ultra | 1 | 125 | 500 | 20 | 480 | 10 kit | 48 kits
Bleach (L) | 0.0015 | 0.1875 | 0.75 | 1L | -0.25 | 4L bottle | 0 bottles
Notes: EDIT

## Slide 50: ASSUMPTIONS FOR CALCULATION #3
Quarterly Supply requirements for Xpert MTB/RIF Ultra testing |  |  |  |  |  |  | 
Laboratory Regional reference laboratory |  |  |  |  |  |  | 
Region Western Region |  |  |  | Supply Quarter 3 |  |  | 
District Urban |  |  |  | Year 2016 |  |  | 
Total tests performed in previous quarter, including failed tests (A) |  |  |  |  |  |  | 
Items | Quantity needed per test (B) | Stock for one month (C) =(A/3)*B | Stock for quarter with 1 month buffer (D)= C*4 | Stock on hand (E) | Calculated request (F) = D-E | Order unit (G) | Actual order (H) = F/G and round up
Sputum container |  |  |  | 250 |  | 100 pack | 
Xpert MTB/RIF Ultra |  |  |  | 175 |  | 10 kit | 
Bleach (L) |  |  |  | 3L |  | 4L bottle | 
Notes: EDIT

## Slide 51: ASSUMPTIONS FOR CALCULATION #3
Quarterly Supply requirements for Xpert MTB/RIF Ultra testing |  |  |  |  |  |  | 
Laboratory Regional reference laboratory |  |  |  |  |  |  | 
Region Western Region |  |  |  | Supply Quarter 3 |  |  | 
District Urban |  |  |  | Year 2016 |  |  | 
Total tests performed in previous quarter, including failed tests (A) 756 |  |  |  |  |  |  | 
Items | Quantity needed per test (B) | Stock for one month (C) =(A/3)*B | Stock for quarter with 1 month buffer (D)= C*4 | Stock on hand (E) | Calculated request (F) = D-E | Order unit (G) | Actual order (H) = F/G and round up
Sputum container | 1 | 252 | 1,008 | 250 | 758 | 100 pack | 8 packs
Xpert MTB/RIF Ultra | 1 | 252 | 1,008 | 175 | 833 | 10 kit | 84 kits
Bleach (L) | 0.015 | 0.378 | 1.512 | 3L | -1.488 | 4L bottle | 0 bottles
Notes: EDIT

## Slide 52: DISCUSSION QUESTIONS
What is included in supply chain management?
Why is a physical stock count necessary?
Why is a buffer stock required?
What are the major reasons for stock-outs in your setting?
List two items provided with the GeneXpert MTB/RIF (Ultra) kit?
List two items NOT provided with the GeneXpert MTB/RIF (Ultra) kit?

## Slide 53: KEY MESSAGES
Supply chain management includes:
  Product selection, specification & forecasting
  Procurement and the ordering
  Distribution
  Onsite stock management
  Monitoring the supply chain

## Slide 54: KEY MESSAGES
When forecasting, consider your past consumption rate, your stock on hand, the shelf-life of the ordered material, the lead time, and your storage capacity, in order to assess quantity and frequency of orders
Perform a stock count physically counting each item in the stock at the end of each month by a designated person, using a stock log book

## Slide 55
THANK YOU
© John Rae