## Slide 1: CLINICAL GUIDE TO XPERT MTB/RIF (ULTRA)
MODULE 8 (M8)

## Slide 2: MODULE CONTENTS
Introduction to Xpert MTB/RIF and Xpert MTB/RIF Ultra
Recommended diagnostic algorithms with Xpert MTB/RIF (Ultra)*
Sputum collection and reporting essentials
Treatment and follow-up testing
* Refers to Xpert MTB/RIF and Xpert MTB/RIF Ultra

## Slide 3: LEARNING OBJECTIVES
At the end of this module, you will be able to:
Describe the role of Xpert MTB/RIF (Ultra) testing in diagnosis of TB and rifampicin resistant (RR) TB
Explain and discuss your country TB diagnostic algorithm (or the WHO preferred algorithms) for diagnosis and management of TB and RR / MDR-TB
Understand the use of the WHO reporting codes for Xpert MTB/RIF (Ultra)

## Slide 4: CONVENTIONAL DIAGNOSTIC METHODS FOR DETECTION OF TB AND RIFAMPICIN RESISTANCE
Sputum smear microscopy is most commonly used in most resource-limited settings to detect TB. However:
    Microscopy detects acid-fast bacilli (AFB) but does not differentiate M. tuberculosis from other AFB, including non-tuberculous mycobacteria (NTMs)
    It has low sensitivity and can miss many cases of TB, particularly in people with HIV
    It does not detect drug resistance

## Slide 5: CONVENTIONAL DIAGNOSTIC METHODS FOR DETECTION OF TB AND RIFAMPICIN RESISTANCE
Central-level laboratories with strict biosafety measures and highly trained staff are needed for performing culture and detecting drug resistance
TB culture and culture based (phenotypic) drug susceptibility testing (DST) are time-consuming methods. Results may be delayed by several weeks
However, TB culture and phenotypic DST have high sensitivity and a broad spectrum of first and second line TB drugs can be tested

## Slide 6: INTRODUCTION TO XPERT MTB/RIF
GeneXpert Xpert MTB/RIF:
    A molecular test that is able to detect both TB and rifampicin resistance in a single test in less than 2 hours
    Much more sensitive than smear microscopy for detection of TB, including HIV-associated TB. Sensitivity is similar to solid LJ culture
    Does not detect NTMs, unlike smear microscopy
    Other tests (e.g. HIV, HCV etc.) are available on the GeneXpert platform

## Slide 7
Boehme CC et al. N Engl J Med 2010;363:1005-1015.
Procedure for the Xpert MTB/RIF test
Notes: Figure 2. Assay Procedure for the MTB/RIF Test. Two volumes of sample treatment reagent are added to each volume of sputum. The mixture is shaken, incubated at room temperature for 15 minutes, and shaken again. Next, a sample of 2 to 3 ml is transferred to the test cartridge, which is then loaded into the instrument. All subsequent steps occur automatically. The user is provided with a printable test result, such as “MTB detected; RIF resistance not detected.” PCR denotes polymerase chain reaction.

## Slide 8: INSERT YOUR COUNTRY ALGORITHM
Adapt according to NTP guidelines in your country

## Slide 9: ALGORITHM 1: PREFERRED ALGORITHM FOR UNIVERSAL PATIENT ACCESS TO RAPID TESTING TO DETECT MTB AND RIFAMPICIN RESISTANCE
Reference: GLI model TB diagnostics algorithms
http://www.stoptb.org/wg/gli/
1 Persons to be evaluated for TB include adults and children with signs or symptoms suggestive of TB or with a chest X-ray with abnormalities suggestive of TB. This algorithm may also be followed for the detection of MTB using CSF, lymph node and other tissue specimen from persons being evaluated for extrapulmonary TB. For persons being evaluated for TB who are HIV positive and have CD4 counts ≤100 cells/μl or are seriously ill, see Algorithm 4.
2 Programmes may consider collecting two specimens upfront. The first specimen should be promptly tested using the Xpert MTB/RIF test. The second specimen may be used for the additional testing described in this algorithm. For persons being evaluated for pulmonary TB, sputum is the preferred specimen.
3 Patients at high risk for multidrug-resistant TB (MDR-TB) include previously treated patients including those who had been lost to follow-up, relapsed, and failed a treatment regimen; non-converters (smear positive at end of intensive phase); MDR-TB contacts; and any other MDR-TB risk groups identified in the country.
4 Patients should be initiated on a first-line regimen according to national guidelines. A sample may be sent for molecular or phenotypic DST for isoniazid if the patient has been previously treated with isoniazid or if there is a high prevalence of isoniazid resistance not associated with rifampicin resistance (i.e., isoniazid mono- or poly-resistance) in this setting or for DST for rifampicin if rifampicin resistance is still suspected.
5 Repeat Xpert MTB/RIF test at the same testing site with a fresh specimen. Interpret the result of the repeat test as shown in this algorithm. Use the result of the second Xpert MTB/RIF test for clinical decisions.
6 Further investigations for TB may include chest X-ray, additional clinical assessments, clinical response following treatment with broad-spectrum antimicrobial agents, repeat Xpert MTB/RIF testing, or culture.
7 Repeat Xpert MTB/RIF test at the same testing site with a fresh specimen. Use the rifampicin result of the second Xpert MTB/RIF test in this algorithm for a decision(s) regarding choice of regimen (first line or second line regimen).

## Slide 10: DIAGNOSTIC ALGORITHM (1)
Algorithm 1 is the preferred algorithm for testing in support of the diagnosis of TB in individuals being evaluated for pulmonary TB and incorporates the goals of the End TB Strategy for the use of WRDs and universal DST
Algorithm 1 should be followed in any setting where Xpert MTB/RIF testing is available on site or when testing can be accessed through a reliable referral system with short turnaround time
The Xpert MTB/RIF test is not recommended as a test to monitor treatment
Reference: GLI model TB diagnostics algorithms
http://www.stoptb.org/wg/gli/

## Slide 11: ALGORITHM 3: ALGORITHM FOR TESTING FOR SECOND-LINE DRUG RESISTANCE AMONG RIFAMPICIN-RESISTANT TB OR MDR-TB PATIENTS
Reference: GLI model TB diagnostics algorithms
http://www.stoptb.org/wg/gli/
1 Patients may be initiated on the shorter MDR-TB regimen if the patient is assessed as being at low risk of having resistance to FQs and to SLIDs and meets the eligibility requirements. In patients at high risk of resistance or in settings with high underlying prevalence of resistance to FQs or SLIDs, selection or design of the treatment regimen to initiate may be guided by SL-LPA if the results can be obtained rapidly. See WHO Guidelines for the programmatic management of drug-resistant tuberculosis, 2016 update.
2 Diagnostic accuracy is similar when SL-LPA is performed directly on sputum or from cultured isolates. SL-LPA can be used on smear-positive or smear-negative specimens although a higher indeterminate rate will occur when testing smear-negative specimens.
3 The shorter MDR-TB regimen may be used in MDR-TB patients who do not have the following conditions: 1) confirmed resistance, or suspected ineffectiveness, to a medicine (except isoniazid) in the shorter MDR-TB regimen for which there is reliable DST, 2) previous exposure for >one month to a second-line medicine included in the shorter MDR-TB regimen, 3) intolerance to one or more medicines in the shorter MDR-TB regimen or increased risk of toxicity, 4) pregnancy, or 5) extrapulmonary disease.

## Slide 12: DIAGNOSTIC ALGORITHM (3)
Algorithm 3 is for further evaluation of patients with RR-TB or MDR-TB.
All patients with RR-TB or MDR-TB should be started on a second-line regimen
The results of DST for FQs and SLIDs should ideally be known for all RR-TB and MDR-TB patients before starting treatment, although this testing should not delay the start of treatment
If SL-LPA is not available, patients should be treated according to national guidelines. Patients may be evaluated for the use of a shorter MDR-TB regimen using criteria such as country drug-resistance patterns and the patient’s treatment history.
Reference: GLI model TB diagnostics algorithms
http://www.stoptb.org/wg/gli/

## Slide 13: XPERT MTB/RIF ULTRA
GeneXpert MTB/RIF Ultra
    Follows the same procedure as the Xpert MTB/RIF test
    Next-generation test with improved sensitivity and detection of RR particularly in smear-negative culture-positive specimens and in specimens from HIV-infected patients
    Can detect non-replicating or non-viable bacilli present particularly in patients with recent history of TB, reducing the overall specificity of Xpert MTB/RIF Ultra in high-burden TB settings

## Slide 14: XPERT MTB/RIF ULTRA
  GeneXpert MTB/RIF Ultra
    Improved sensitivity for extrapulmonary specimens and pediatrics
    Extrapulmonary specimens include*
    Cerebrospinal fluid (CSF)
    Lymph nodes
    Tissue specimens
* http://www.stoptb.org/wg/gli/assets/documents/GLI_ultra.pdf

## Slide 15: INSERT YOUR COUNTRY ALGORITHM
Adapt according to NTP guidelines in your country

## Slide 16: DIAGNOSTIC ALGORITHM (1A)
1 Persons to be evaluated for TB include adults and children with signs or symptoms suggestive of TB or with a chest X-ray with abnormalities suggestive of TB. This algorithm may also be followed for the diagnosis of extrapulmonary TB using CSF, lymph node and other tissue specimen. The evaluation should include determining the person’s age, HIV-infection status, and possibility of a history of TB treatment.
2 MTB detected (not trace) includes MTB detected high, moderate, low, or very low. Follow Algorithm 1 for interpretation and follow-up testing.
3 MTB detected trace results do not provide any information regarding rifampicin susceptibility or resistance.
4 PLHIV include persons who are HIV positive or whose HIV status is unknown, but who present with strong clinical evidence of HIV infection in settings where there is a high prevalence of HIV or among members of a risk group for HIV. For all people with unknown HIV status, HIV testing should be performed according to national guidelines.
5 Patients should be initiated on a rst-line regimen according to national guidelines unless the patient is at very high risk of having MDR-TB or if a second Ultra assay indicates rifampicin resistance. Such patients should be initiated on an MDR-TB regimen.
6 For adults who successfully completed a course of therapy within the past 2 years (i.e., recent TB treatment), the possibility of both Ultra trace results being false-positive results because of the presence of non-viable bacilli must be considered. Clinical decisions must be made on all available information and clinical judgment; further investigations for TB may include chest X-ray, additional clinical assessments, clinical response following treatment with broad-spectrum antimicrobial agents, repeat Ultra testing, or culture.
7 Further investigations for TB may include chest X-ray, additional clinical assessments, clinical response following treatment with broad-spectrum antimicrobial agents, repeat Ultra testing, or culture.
Reference: GLI model TB diagnostics algorithms
http://www.stoptb.org/wg/gli/

## Slide 17: DIAGNOSTIC ALGORITHM (1A)
Algorithm 1A has been developed by GLI based on the conclusions of the WHO Report on the use of Xpert MTB/RIF Ultra
Xpert MTB/RIF Ultra test is used as the initial diagnostic test for all adults and children, regardless of HIV status, with signs or symptoms consistent with pulmonary TB or with a chest X-ray with abnormalities suggestive of TB
Reference: GLI model TB diagnostics algorithms
http://www.stoptb.org/wg/gli/
The considerations for the use of the Xpert MTB/RIF Ultra assay are the same as for the Xpert MTB/RIF assay as described in the decision tree for Algorithm 1
The interpretation of ‘MTB detected trace’ results and necessary follow-up testing are described in this algorithm

## Slide 18: SPUTUM SPECIMEN COLLECTION
Use appropriate container for specimen collection (sterile, translucent, combustible, leak-proof, screw-capped, wide-mouthed).
Make sure that specimen details on container match the Lab Request Form
Collection of sputum should be supervised

## Slide 19: SPUTUM SPECIMEN COLLECTION: GOOD QUALITY
Obtaining an adequate quantity of good quality sputum is critical to ensuring accurate test results
For best results, obtain >1ml of purulent/mucoid sputum
Purulent
Mucoid
Bloodstained
© A. van Deun

## Slide 20: SPUTUM SPECIMEN COLLECTION: POOR QUALITY
Poor quality specimens give poor quality results
Salivary (thin, watery, or comprised mainly of bubbles)
© A. van Deun

## Slide 21: LABORATORY REQUEST FORM*: EXAMPLE
To be completed by person requesting the test
Replace with your country’s request form
* WHO Definitions and reporting framework for tuberculosis – 2013 revision

## Slide 22: LABORATORY REQUEST FORM: CONTENT
Name of treatment unit
Date of request
Patient information (i.e. name, sex, age, address, and patient/suspect register number)
Number of specimens and specimen type sent for testing
Date of collection of specimen(s)
Name of test to be performed [e.g. Xpert MTB/RIF (Ultra)]
Reason for examination (i.e. diagnosis or follow-up)
Clinical information
Type of patient (i.e. retreatment, MDR, PLHIV, New etc.)
Signature of person requesting examination
Adapt according to NTP guidelines in your country

## Slide 23: SPECIAL CONSIDERATIONS FOR XPERT MTB/RIF ULTRA*
WHO recommends repeat testing of Xpert MTB/RIF Ultra trace call results
Depending on the algorithm, information on the patient category (e.g. pediatric, history of previous treatment) may be required. Patient categories are often included on request forms, but are incompletely or inconsistently completed
Establish a numbering system to identify repeat samples from the same patient, in order to monitor the proportion and performance of repeat tests
* http://www.stoptb.org/wg/gli/assets/documents/GLI_ultra.pdf
Adapt according to NTP guidelines in your country

## Slide 24: RECORDING XPERT MTB/RIF RESULTS
Xpert MTB/RIF result | Reported result | WHO code
MTB Detected High Rifampicin Resistance Not Detected | MTB detected, rifampicin susceptible | T
MTB Detected Medium Rifampicin Resistance Not Detected |  | 
MTB Detected Low Rifampicin Resistance Not Detected |  | 
MTB Detected Very Low Rifampicin Resistance Not Detected |  | 
MTB Detected Very low Rifampicin Resistance Indeterminate | MTB detected, rifampicin indeterminate | TI
MTB Detected High Rifampicin Resistance Detected | MTB detected, rifampicin resistant | RR
MTB Detected Medium Rifampicin Resistance Detected |  | 
MTB Detected Low Rifampicin Resistance Detected |  | 
MTB Detected Very Low Rifampicin Resistance Detected |  | 
MTB Not Detected | MTB not detected | N
Invalid / Error / No Result | Inconclusive | I
Notes: Viewing results could go into module 2 so module is omni specific without test results

## Slide 25: LABORATORY REGISTER EXAMPLE* : XPERT MTB/RIF
Adapt according to NTP guidelines in your country
* WHO Definitions and reporting framework for tuberculosis – 2013 revision

## Slide 26: LABORATORY REGISTER: CONTENT
Laboratory serial number
Date specimen received
Patient's information (i.e., name, sex, age, address, treatment unit and register number)
HIV status
Patient previously treated for TB
Examination type (e.g., diagnosis or follow-up)
Examination result / date (see WHO category)
Remarks (e.g. Xpert MTB/RIF indeterminate result, indicate error code or “invalid”)
Adapt according to NTP guidelines in your country

## Slide 27: SPECIAL CONSIDERATIONS FOR XPERT MTB/RIF ULTRA*
There is an additional result category for Xpert MTB/RIF Ultra trace that differentiates it from the TI category
The TI category should still be used for “MTB detected, RIF resistance indeterminate” results other than the trace calls (i.e., where the semi-quantitative result is very low or higher)
For Ultra, the following abbreviation should be used for trace calls:
TT = MTB detected (trace), RIF resistance indeterminate
* http://www.stoptb.org/wg/gli/assets/documents/GLI_ultra.pdf

## Slide 28: RECORDING XPERT MTB/RIF ULTRA RESULTS
Xpert MTB/RIF result | Reported result | WHO code
MTB Detected High Rifampicin Resistance Not Detected | MTB detected, rifampicin susceptible | T
MTB Detected Medium Rifampicin Resistance Not Detected |  | 
MTB Detected Low Rifampicin Resistance Not Detected |  | 
MTB Detected Very Low Rifampicin Resistance Not Detected |  | 
MTB Detected Very low Rifampicin Resistance Indeterminate | MTB detected, rifampicin indeterminate | TI
MTB Detected High Rifampicin Resistance Detected | MTB detected, rifampicin resistant | RR
MTB Detected Medium Rifampicin Resistance Detected |  | 
MTB Detected Low Rifampicin Resistance Detected |  | 
MTB Detected Very Low Rifampicin Resistance Detected |  | 
MTB Detected (Trace), RIF Resistance Indeterminate | MTB detected trace | TT
MTB Not Detected | MTB not detected | N
Invalid / Error / No Result | Inconclusive | I
Notes: Viewing results could go into module 2 so module is omni specific without test results

## Slide 29: TREATMENT
    Refer to your country treatment guidelines & TB diagnostic algorithm:
    For patients detected by Xpert MTB/RIF (Ultra), start patients immediately on first-line treatment
    For patients with RR detected by Xpert MTB/RIF (Ultra), start patients immediately on an MDR-TB regimen
    Collect another specimen for further DST to determine the full resistance profile
    While Xpert MTB/RIF (Ultra) is able to provide results rapidly, systems must be in place for efficient sample & patient referral and reporting of results

## Slide 30: TESTING FOR TREATMENT FOLLOW-UP
Xpert MTB/RIF (Ultra) can not be used for monitoring and follow up of patients during treatment
  Continue to use smear and/or culture according to guidelines for follow up of patients on treatment

## Slide 31: EXERCISE: CLINICAL CASE STUDIES
Purpose
To review Xpert MTB/RIF clinical case studies suggest actions to address the situations presented
Total time
50 minutes: about 15 minutes discussion in small groups, 20 minutes to report back to the large group, 10 minutes group discussions
Process
Work in four groups
On the worksheet provided (1 scenario per group) review the scenario and address the questions
Select a spokesperson and share your findings with the group

## Slide 32: KEY MESSAGES
Xpert MTB/RIF (Ultra) are more sensitive for TB detection than smear microscopy
Xpert MTB/RIF (Ultra) can rapidly and accurately diagnose TB and RR, but can not be used for monitoring or follow-up testing of patients on treatment
Collection of good quality sputum is essential for good diagnosis, using Xpert and all other lab tests
WHO recommends using standard codes for reporting Xpert MTB/RIF (Ultra) results

## Slide 33: KEY MESSAGES
    Refer to your country treatment guidelines & TB diagnostic algorithm:
    For patients detected by Xpert MTB/RIF (Ultra), start patients immediately on first-line treatment
    For patients with RR detected by Xpert MTB/RIF (Ultra), start patients immediately on an MDR-TB regimen
    Xpert MTB/RIF (Ultra) can not be used for monitoring / follow up of patients during treatment

## Slide 34
THANK YOU
© John Rae